## Slide 1: NetPulse: Real-Time Network Packet Capture, Protocol Decoding and Live Streaming Dashboard
BCSE308P | Computer Networks Lab | Fall Semester 2026-27
Aditya Pratap (24BKT0132)
B.Tech CSE (Blockchain Technology) | School of Computer Science and Engineering, VIT | October 2026
Ethernet
IPv6
Hop-by-Hop
ICMPv6 (MLD)
One IPv6 packet, decoded layer by layer
Notes: Introduce the project: NetPulse is a small C++ and libpcap packet analyser with a live web dashboard. The coloured row shows an IPv6 packet whose Hop-by-Hop header hides the real protocol; decoding that correctly is the heart of the project.

## Slide 2: Why simple sniffers fail
Packet capture underpins troubleshooting, monitoring and security. A baseline libpcap sniffer breaks in three ways.
IPv6 shown as “Protocol 0”
Hop-by-Hop headers (MLD, Router Alert) hide the real protocol, so ICMPv6 type and ports are lost.
Garbage on the “any” interface
Linux cooked frames are read as Ethernet, so every offset is wrong.
Self-capture feedback storm
POSTs to the backend on port 3000 are captured and posted again, without bound.
Notes: These are the three real failures I hit in the first version: IPv6 packets reported as Protocol 0, wrong decoding when capturing on the any interface, and a feedback storm because the sniffer's own HTTP posts to port 3000 were captured again.

## Slide 3: Same packet, two decoders
Packet sent | Baseline prints | Proposed prints
Hop-by-Hop + MLDv2 report | HOPOPT | ICMPv6 (MLDv2 Report)
Hop-by-Hop + TCP SYN to port 80 | HOPOPT | TCP (HTTP) fd00::6:40001 → ::1:80
Destination Options + UDP to port 53 | Proto 60 | UDP (DNS) fd00::7:40002 → ::1:53
0 %
Baseline: extension-header packets identified correctly, in every run at every load
100 %
Proposed: extension-header packets identified correctly, in every run at every load
Notes: Same three crafted packets through both decoders. The baseline prints HOPOPT or Proto 60 and loses the ports. The proposed decoder walks the extension header chain and prints the real protocol with ports. Measured across 5 runs and 3 load levels: 0 percent versus 100 percent.

## Slide 4: Proposed novelty
Aspect | Baseline | Proposed
IPv6 upper layer | Reads ip6_nxt only | Walks 6 extension header types to the real protocol
Link layer | Ethernet only | Ethernet + 802.1Q, Linux cooked v1/v2, loopback
Self-capture | None | BPF “not (tcp port 3000)” + user-space port check
Blocking | Unbounded sends | 250 ms socket timeouts
DNS visibility | None | UDP forwarder reports each query
Notes: Five differences between the baseline and NetPulse. The contribution is an engineered, evaluated combination rather than a new protocol: extension-header-aware decoding, datalink-aware framing, a self-capture guard, bounded blocking and DNS telemetry.

## Slide 5: Architecture and pipeline
Network interface
eth0, lo, any
frames
C++ capture
sniffer_http, sniffer, dns_server
HTTP POST
Node.js backend
Express :3000, Socket.IO
WebSocket
Browser dashboard
live list, filters, KPIs
Decode pipeline, per packet
1
Read datalink type
2
Parse link header
3
IPv4, IPv6 or ARP
4
Walk IPv6 extension headers
5
Decode TCP, UDP, ICMP
6
Self-traffic check, then POST
Extension headers handled: Hop-by-Hop, Routing, Fragment, Destination Options, AH, Mobility. Every step is bounded by the captured length.
Notes: Top row: the data path from the network interface to the browser. Bottom row: what happens to each packet inside the C++ program. Step 4 is the extension header walk that fixes the Protocol 0 problem. Step 6 combines the kernel BPF filter and the user-space port check that stop the feedback storm.

## Slide 6: Implementation and testbed
1,560
lines of C++, 3 programs
5
datalink types decoded
6
IPv6 extension header types
3
load scenarios, 5 runs each
Testbed
Ubuntu 24.04 host, 1 vCPU, loopback
2,000-packet Scapy pool replayed with tcpreplay
Ground truth by construction, checked with tcpdump
Scenarios
50, 1,000 and 10,000 packets/s, 20 s per run
40 % IPv6 with extension headers, 20 % IPv6, 35 % IPv4, 5 % ARP
Baseline = same code without the extension-header walk and the self-capture guard
Notes: The code is about 1,560 lines of C++ plus a Node.js backend. Be upfront about the environment: the measurements were taken on a single-vCPU Ubuntu host over the loopback interface, so absolute throughput is specific to that host; the baseline-versus-proposed comparison is what matters. The experiment scripts are provided so the runs can be repeated on the Kali VM.

## Slide 7: Results: baseline vs proposed
Metric | S1 50 pkt/s |  | S2 1,000 pkt/s |  | S3 10,000 pkt/s | 
 | Base | Prop | Base | Prop | Base | Prop
M1 Ext-header accuracy (%) | 0.0 ± 0.0 | 100.0 ± 0.0 | 0.0 ± 0.0 | 100.0 ± 0.0 | 0.0 ± 0.0 | 100.0 ± 0.0
M2 Amplification (×) | 36.80 ± 0.70 | 1.00 ± 0.00 | 1.95 ± 0.02 | 1.00 ± 0.00 | 0.20 ± 0.00 | 0.20 ± 0.00
M3 Kernel drops (%) | 87.25 ± 0.04 | 0.00 ± 0.00 | 87.98 ± 0.09 | 0.00 ± 0.00 | 91.98 ± 0.05 | 78.98 ± 0.32
M4 Delivery (%) | 99.80 ± 0.00 | 100.00 ± 0.00 | 99.80 ± 0.00 | 99.87 ± 0.00 | 99.80 ± 0.00 | 99.80 ± 0.00
M5 Coverage (%) | 13.7 ± 0.7 | 100.0 ± 0.0 | 8.1 ± 0.1 | 100.0 ± 0.0 | 3.1 ± 0.2 | 19.8 ± 0.5
Mean ± SD of 5 runs, 20 s each. M1 is measured only on the 40 % of packets that carry IPv6 extension headers; on plain IPv6 both builds were correct. M2 streamed ÷ offered, M3 kernel drops, M4 delivery, M5 IPv6 traffic analysed. Single-vCPU Ubuntu host, loopback.
Notes: Read the table by metric. M1: 0 versus 100 percent everywhere. M2: the baseline storm amplifies traffic 36.8 times at 50 packets per second; the proposed build streams exactly what is offered. At 10,000 packets per second both builds hit the same processing ceiling, so M2 ties at 0.20; the difference shows up in M5 coverage.

## Slide 8: Kernel drops and coverage
Chart: M3 Kernel drop rate (%)
| S1 50/s | S2 1,000/s | S3 10,000/s
Baseline | 87.25 | 87.98 | 91.98
Proposed | 0 | 0 | 78.98
Chart: M5 Offered IPv6 traffic analysed (%)
| S1 50/s | S2 1,000/s | S3 10,000/s
Baseline | 13.7 | 8.1 | 3.1
Proposed | 100 | 100 | 19.8
Link layer check: on the “any” interface an Ethernet-only parser decoded 0 of 600 IPv6 packets; the datalink-aware decoder decoded 600 of 600.
Notes: The storm fills the kernel buffer, so the baseline loses roughly 87 to 92 percent of frames in every scenario and analyses only 3 to 14 percent of the offered IPv6 traffic. The proposed build loses nothing at 50 and 1,000 packets per second. At 10,000 packets per second it analyses about 6.5 times as much traffic as the baseline, even though both are saturated.

## Slide 9: Analysis and limitations
What the data shows
Baseline misreported every extension-header packet; proposed got all of them
Without the guard, 50 packets/s became 36.8× traffic as posts were re-captured
Both builds saturate near 1,800 pkt/s on one CPU; proposed analyses 6.5× more at 10,000 pkt/s
Limitations
Non-first IPv6 fragments get false ports (200 of 200 tested)
One TCP connection per packet caps throughput
No flow reassembly or capture timestamps
Dashboard has no authentication or TLS
Notes: Be candid about limits: the 1,800 packets per second ceiling comes from opening one TCP connection per packet on a single CPU, and non-first IPv6 fragments are misread because the code does not check the fragment offset. Both were measured, not just suspected.

## Slide 10: Conclusion and future work
Conclusion
Three baseline defects removed in a compact, explainable pipeline
Extension-header packets identified: 0 % to 100 %
Amplification 36.8× to 1.0× and 0 % kernel drops up to 1,000 pkt/s
Future work
Persistent connection or batching
Flow tracking and TCP analysis
Offline pcap mode, anomaly detection
Authentication and TLS
References: RFC 8200 | RFC 9098 | RFC 7112 | McCanne and Jacobson, BPF (1993) | libpcap and tcpdump
Notes: Close by restating the result: the three defects are fixed, measured against a baseline with repeated runs. Mention the first future step, a persistent connection or batching, because it addresses the measured throughput ceiling. Then take questions.